## Slide 1: FPGA seminar
2023-02-02
Wonjun-Jeong

## Slide 2: chapter
Part1. What is FPGA?
Part2. FPGA coding

## Slide 3: 1.What is FPGA?

## Slide 4: What is FPGA?
FPGA is Field-Programmable Gate Array
FPGA can process operations in parallel
FPGA can calculate fastly
FPGA designer could design FPGA’s physical circuits
FPGA can reprogram the designed logic
FPGA’s feature

## Slide 5: Logic circuit on an FPGA
Or gate
And gate
xor gate
Intput 1 | Input 2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Intput 1 | Input 2 | output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Intput 1 | Input 2 | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Or gate
Nand gate
Input | Output
1 | 0
0 | 1
Intput 1 | Input 2 | output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 6: Boolean algebra equation
dot mean ‘and’
= and
Plus sign mean ‘or’
+ = or
Line over the top mean ‘not’
= not A
A
B output
C

## Slide 7: Look-Up Table
LUT is digital circuit that can be used to implement any Boolean function in FPGA design
Input are connected to the FPGA’s programmable interconnect points
LUT
defines and directs the behavior of the combinatorial logic of based on VHDL or Verilog code
Basically serve to act like logic gates in various combinations
use a LUT to simply get all the possible
Output is generated by the LUT’s internal logic

## Slide 8: Flip - Flop
Flip-Flop is a circuit that can store and maintain 1 bit of information
D Flip-Flop captures the value of input D at the edge of the clock and reflects in Q
D Flip-Flop
D
Q
>
output
Data in
Clock
Clock | D | Q
Rising Edge | 0 | 0
Rising Edge | 1 | 1
Rising Edge | Rising Edge | 0
Rising Edge | Falling Edge | 1
Data in
Clock
Q
Related to delay

## Slide 9: Flip - Flop
Set up time : Minimum time required to determine whether the waveform in Data is High or Low(before switching)
Hold time : Minimum time for determined results to be maintained(after switching)
Data in
Clock
Q
Set up time
Set up time
Hold time
Hold time
0
1
0.7
0.3
high
low

## Slide 10: Debounce
‘Debouncing’ is appropriate delay time used to eliminate vibrational noise when push switch
Expected behavior
stable
Actual
behavior
stable
bounce
Push switch
Push switch

## Slide 11: 2.FPGA coding

## Slide 12: Switch LED(Verilog)
Module Switches_To_Leds
(input i_Switches_1,
input i_Switches_2,
input i_Switches_3,
input i_Switches_4,
Output o_LED_1,
Output o_LED_2,
Output o_LED_3,
Output o_LED_4);
assign o_LED_1 = i_Switch_1;
assign o_LED_2 = i_Switch_2;
assign o_LED_3 = i_Switch_3;
assign o_LED_4 = i_Switch_4;
Endmodule // Switches_To_LEDs
Verilog Code
sw1
sw2
sw3
sw4
D1
D2
D3
D4
FPGA

## Slide 13: Switch LED(Verilog)
Module Switches_To_Leds
(input i_Switches_1,
input i_Switches_2,
input i_Switches_3,
input i_Switches_4,
Output o_LED_1,
Output o_LED_2,
Output o_LED_3,
Output o_LED_4);
assign o_LED_1 = i_Switch_1;
assign o_LED_2 = i_Switch_2;
assign o_LED_3 = i_Switch_3;
assign o_LED_4 = i_Switch_4;
Endmodule // Switches_To_LEDs
Verilog Code
sw1
sw2
sw3
sw4
D1
D2
D3
D4
FPGA

## Slide 14: SWITCH LED(VHDL)
Library ieee;
Use ieee.std_logic_1164.all
Entity Switches_To_LEDS is
port(
i_Switch_1 : in std_logic;
i_Switch_2 : in std_logic;
i_Switch_3 : in std_logic;
i_Switch_4 : in std_logic;
o_LED1 : out std_logic;
o_LED2 : out std_logic;
o_LED3 : out std_logic;
o_LED4 : out std_logic);
End entity Switches_To_LEDs;
Architecture RTL of Switches_To_LEDs is
Begin
o_LED_1 <= i_Switch_1;
o_LED_2 <= i_Switch_1;
o_LED_3 <= i_Switch_1;
o_LED_4 <= i_Switch_1;
End archticture RTL:
VHDL code
sw1
sw2
sw3
sw4
D1
D2
D3
D4
FPGA

## Slide 15: Switch LED(VHDL)
Library ieee;
Use ieee.std_logic_1164.all
Entity Switches_To_LEDS is
port(
i_Switch_1 : in std_logic;
i_Switch_2 : in std_logic;
i_Switch_3 : in std_logic;
i_Switch_4 : in std_logic;
o_LED1 : out std_logic;
o_LED2 : out std_logic;
o_LED3 : out std_logic;
o_LED4 : out std_logic);
End entity Switches_To_LEDs;
Architecture RTL of Switches_To_LEDs is
Begin
o_LED_1 <= i_Switch_1;
o_LED_2 <= i_Switch_1;
o_LED_3 <= i_Switch_1;
o_LED_4 <= i_Switch_1;
End archticture RTL:
sw1
sw2
sw3
sw4
D1
D2
D3
D4
FPGA
VHDL code

## Slide 16: Toggle Switch
Module Clocked_Logic
(input i_Clk
input i_Switches_1,
Output o_LED_1);
Reg r_LED_1 = 1’b0;
Reg r_Switch_1 = 1’b0;
Always @(posedge i_Clk)
begin
r_Switch_1 <= i_Switch_1
if (i_Switch_1 == 1’b0 && r_Switch_1 == 1’b1)
begin
r_LED_1 <= ~r_LED1;
end
end
assign o_LED_1 = r_LED_1;
Endmodule // Clocked_Logic
Verilog Code
VHDL Code
Library ieee;
Use ieee.std_logic_1164.all
Entity clocked_Logic is
port(
i_Clk : in std_logic;
i_Switch_1 : in std_logic;
o_LED1 : out std_logic);
End entity Switches_To_LEDs;
Architecture RTL of clocked_Logic is
signal r_LED1 : std_logic := ‘0’
signal r_Switch_1 : std_logic :=‘0’
begin
p_Register : process(i_Clk) then
begin
if rising_edge(i_Clk) then
r_switch_1 <= i_Switch_1;
if i_switch_1 = ‘0’ and r_switch_1 = ‘1’ then
r_LED_1 <= not r_LED_1;
end if;
end if;
End process p_Register;
o_LED_1 <= r_LED_1;
End archticture RTL: p_Register

## Slide 17: Toggle and Debounce(Verilog)
Module Clocked_Logic
(input i_Clk
input i_Switches_1,
Output o_LED_1);
reg r_LED_1 = 1’b0;
reg r_Switch_1 = 1’b0;
wire w_Switch_1;
Debounce_Switch Instance
(.i_Clk(i_clk),
.i_Switch(i_Switch_1),
.o_Switch(w_Switch_1));
Always @(posedge i_Clk)
begin
r_Switch_1 <= w_Switch_1
if (w_Switch_1 == 1’b0 && r_Switch_1 == 1’b1)
begin
r_LED_1 <= ~r_LED1;
end
end
assign o_LED_1 = r_LED_1;
Endmodule // Clocked_Logic
Verilog Code
Module Debounce_Switch
(input i_Clk,
input i_Switch,
output o_Switch);
parameter c_DEBOUNCE_LIMIT = 250000
reg r_State = 1’b0;
reg [17:0] r_Count=0;
always @(posedge i_Clk)
begin
if (i_Switch !== r_Stage && r_Count < c_DEBOUNCE_LIMIT)
r_Count <= r_count +1;
elsse if (r_Count == c_DEBOUNCE_LIMIT)
begin
r_Count <= 0;
r_Stage <= i_Switch;
end
else
r_Count <= 0;
end
assign o_Switch = r_Stage
endmodule

## Slide 18: Toggle and Debounce(Verilog)
Module Clocked_Logic
(input i_Clk
input i_Switches_1,
Output o_LED_1);
reg r_LED_1 = 1’b0;
reg r_Switch_1 = 1’b0;
wire w_Switch_1;
Debounce_Switch Instance
(.i_Clk(i_clk),
.i_Switch(i_Switch_1),
.o_Switch(w_Switch_1));
Always @(posedge i_Clk)
begin
r_Switch_1 <= w_Switch_1
if (w_Switch_1 == 1’b0 && r_Switch_1 == 1’b1)
begin
r_LED_1 <= ~r_LED1;
end
end
assign o_LED_1 = r_LED_1;
Endmodule // Clocked_Logic
Verilog Code
Module Debounce_Switch
(input i_Clk,
input i_Switch,
output o_Switch);
parameter c_DEBOUNCE_LIMIT = 250000
reg r_State = 1’b0;
reg [17:0] r_Count=0;
always @(posedge i_Clk)
begin
if (i_Switch !== r_Stage && r_Count < c_DEBOUNCE_LIMIT)
r_Count <= r_count +1;
elsse if (r_Count == c_DEBOUNCE_LIMIT)
begin
r_Count <= 0;
r_Stage <= i_Switch;
end
else
r_Count <= 0;
end
assign o_Switch = r_Stage
endmodule

## Slide 19: Toggle and Debounce(VHDL)
VHDL Code
Library ieee;
Use ieee.std_logic_1164.all
Entity clocked_Logic is
port(
i_Clk : in std_logic;
i_Switch_1 : in std_logic;
o_LED1 : out std_logic);
end entity Switches_To_LEDs;
architecture RTL of clocked_Logic is
signal r_LED1 : std_logic := ‘0’
signal r_Switch_1 : std_logic :=‘0’
signal w_Switch_1 : Std_logic;
begin
Debounce_Inst: entity work.Debounce_Switch
port map(
i_Clk => i_Clk,
i_Switch => i_Switch_1,
o_Switch => w_Switch_1);
p_Register : process(i_Clk) then
begin
if rising_edge(i_Clk) then
r_switch_1 <= w_Switch_1;
if w_switch_1 = ‘0’ and r_switch_1 = ‘1’ then
r_LED_1 <= not r_LED_1;
end if;
end if;
End process p_Register;
o_LED_1 <= r_LED_1;
End archticture RTL: p_Register
Library ieee;
use ieee.std_logic_1164.all
use ieee.numeric_std.all
Entity Debounce_Switch is
port(
i_Clk : in std_logic;
i_Switch : in std_logic;
o_Switch : out std_logic
);
End entity Debounce_Switch;
Architecture RTL of Debounce_Switch is
constant c_DEBOUNCE_LIMIT : integer := 250000;
signal r_State : std_logic := ‘0’;
singal r_Count : integer range 0 to c_DEBOUNCE_LIMIT :=0;
Begin
p_Debounce : process(i_Clk) then
begin
if rising_edge(i_Clk) then
if (i_Switch /= r_State and r_Count < c_DEBOUNCE_LIMIT) then
r_Count <= r_Count +1;
elsif r_Count = c_DEBOUNCE_LIMIT then
r_Stage <= i_Switch;
r_count <= 0;
end if;
endif
end process p_Debounce;
o_Switch <= r_stage;
end architecture RTL;

## Slide 20: Toggle and Debounce(VHDL)
VHDL Code
Library ieee;
Use ieee.std_logic_1164.all
Entity clocked_Logic is
port(
i_Clk : in std_logic;
i_Switch_1 : in std_logic;
o_LED1 : out std_logic);
end entity Switches_To_LEDs;
architecture RTL of clocked_Logic is
signal r_LED1 : std_logic := ‘0’
signal r_Switch_1 : std_logic :=‘0’
signal w_Switch_1 : Std_logic;
begin
Debounce_Inst: entity work.Debounce_Switch
port map(
i_Clk => i_Clk,
i_Switch => i_Switch_1,
o_Switch => w_Switch_1);
p_Register : process(i_Clk) then
begin
if rising_edge(i_Clk) then
r_switch_1 <= w_Switch_1;
if w_switch_1 = ‘0’ and r_switch_1 = ‘1’ then
r_LED_1 <= not r_LED_1;
end if;
end if;
End process p_Register;
o_LED_1 <= r_LED_1;
End archticture RTL: p_Register
Library ieee;
use ieee.std_logic_1164.all
use ieee.numeric_std.all
Entity Debounce_Switch is
port(
i_Clk : in std_logic;
i_Switch : in std_logic;
o_Switch : out std_logic
);
End entity Debounce_Switch;
Architecture RTL of Debounce_Switch is
constant c_DEBOUNCE_LIMIT : integer := 250000;
signal r_State : std_logic := ‘0’;
singal r_Count : integer range 0 to c_DEBOUNCE_LIMIT :=0;
Begin
p_Debounce : process(i_Clk) then
begin
if rising_edge(i_Clk) then
if (i_Switch /= r_State and r_Count < c_DEBOUNCE_LIMIT) then
r_Count <= r_Count +1;
elsif r_Count = c_DEBOUNCE_LIMIT then
r_Stage <= i_Switch;
r_count <= 0;
end if;
endif
end process p_Debounce;
o_Switch <= r_stage;
end architecture RTL;